## Slide 1
Antonio Di Tecco – Gabriele Martino – Maurizio Pulizzi
Performance Evaluation for Computer Systems and Networks
Analysis of the protocol
Epidemic Broadcast

## Slide 2
2
Epidemic broadcast – Overview and Modeling
Antonio Di Tecco Gabriele Martino Maurizio Pulizzi
Network setup:
Static, flat and multi-hop
Time discrete, one message fit in a slot
Nodes are located with a uniform randomness
Retransmission probability is given by a
Bernullian distribution
Performance indexes:
Broadcast time
Coverage%
Collisions number
NOT INFECTED
INFECTED
IDLE
MSG
*SM &
COUNTER > 1
SM & COUNTER = 1
SENT
SM & MSG UNSENT
* SM = Self message

## Slide 3
3
Preliminary analisys
Antonio Di Tecco Gabriele Martino Maurizio Pulizzi
Affecting factors:
Floor size (X,Y)
Ratio of the two edge of the floor RX|Y
Quantity of nodes N
Retransmission probability Pr
Starter node position
Calibration:
Radius of transmission R = 30m
Perfectioning of a scenario for multi hopping

## Slide 4
4
The room
Antonio Di Tecco Gabriele Martino Maurizio Pulizzi
Scenario:
Dimensions: 125x250 meters
Factors: Probability of retrasmissions and number of nodes
Results:
Minimum density required
For low Pr total coverage is obtained
Hight Pr require more density
Hight Pr converges to lower coverage percentages

## Slide 5
5
Stress test
Antonio Di Tecco Gabriele Martino Maurizio Pulizzi
Small floor (70x70) with lot of nodes (up to 3100) very hight density
The collapse of the coverage never happens
The message is able to spread even at high densities

## Slide 6
For excessive density we have:
Hight number of hops the spread of the message does not take place like wildfire
Hight number of collisions
Hight Broadcast Time
6
High density inefficience
Antonio Di Tecco Gabriele Martino Maurizio Pulizzi

## Slide 7
7
Area and ratio indipendence
Antonio Di Tecco Gabriele Martino Maurizio Pulizzi
For the percentage of coverage we can say that:
the area of the floor has a negligible influence
the shape of the plane has a negligible influence until it becomes too squashed

## Slide 8
8
Broadcast time
Antonio Di Tecco Gabriele Martino Maurizio Pulizzi
Rectangular scenario
Decreasing trend for low P
Increasing trend shows inefficiency
0.9 quantile for more stable samples
Fronts of first point reaching high C%
Minimum points of fronts represent the lowest density for the lowest BT for an high C%

## Slide 9
9
Broadcast time Dependence on Area and Shape
Antonio Di Tecco Gabriele Martino Maurizio Pulizzi
Same ratio between the two edges: 2:1
Incremental Area
Probability of retransmission and density fixed to the minimizing point :
P = 0.4 ; б = 0.0064 N/m2 (200 nodes on the previous case)
Fixed area
Incremental ratio of the two edges: from 1:1 to 1:8
No edges under about 2.5 times the diameter of a coverage area of a node

## Slide 10
10
Broadcast time Dependence on Maximum distance
Antonio Di Tecco Gabriele Martino Maurizio Pulizzi
The real dependence is about the distance between the starter node and farthest ones.
Analisys on distance between starter node positioned at center and corners

## Slide 11
11
The Highway
Antonio Di Tecco Gabriele Martino Maurizio Pulizzi
The propagation is choked
The position of the starter node matters
A lower P is needed

## Slide 12
Question?